FabLab Spinderihallerne 2018
Group Project
based on Keep J.

DELTA CERAMIC/PASTE 3D PRINTER RIG PARTS

(It's just an helpful guide and no responsability is taken for this information so please check all items before ordering for your suitability)

SY42STH47-1684A High Torque Hybrid Stepper Motors (Note: 1.8 step angle, 2 phase, rated voltage 2.8, rated current 1.68, 4.4 kg.cm holding torque, 42 x 42 x 47 mm body, 4 wires - also known as Nema 17 steppers. Go for high torque) / 3 @ £12.00/$21.00 / UK - Zapp Automation http://www.zappautomation.co.uk/en/
SFC12 Precision ground round shaft (12 mm) - Length: 700MM or more (Note: The length of these rods does not seriously alter the settings of the printer) / 6 @ 880dkk / DK - https://3dnielsen.dk/glatte-staalstnger/853-igus-diameter-12mm-swm-d-12-h6-pr-cm.html
LM12UU Linear bearing LM12UU (Note: must fit shafts above) / 6 @ £2.00/$19.90 for 10 / UK - Zapp Automation http://www.zappautomation.co.uk/en/ / https://3dnielsen.dk/lmuu-koblinger/105-lm12uu-1-stk.html
RAMPS 1.4 with mega 2560, LCD Screen / * Mega 2560 core microcontroller (Arduino base) / * RAMPS 1.4 electronics board that sits over the Mega / * You want Stepper motor drivers mounted into the RAMPS board / * LCD display screen with SD card slot and connector cables / (Note: Different LCD screens have different settings in the Marlin firmware) / 1 @ 38,99 € / cd
3 x End stops – there are two types and both work but you need to sort out the wiring.
1 x 100k thermostat to override temperature code in firmware / 1@ 11,25dkk / https://www.trab.dk/da/extruderhotend/183-100k-ohm-ntc-thermistor.html?search_query=100k+thermostat&results=6
GT2 6mm Timing Bælte / 3 @ 121,25 dkk / https://www.trab.dk/da/andet/197-gt2-6mm-timing-baelte.html?search_query=GT2+6mm+Timing+Baelt&results=16
GT2 20 tooth Timing Pulleys x 3 (One for each stepper motor) / Note – Search around you can probably find belts (above) and pulleys together for a good price. / UK - https://www.think3dprint3d.com/Hardware/Belts-and-pulleys/GT2-20-ToothTimingPulley-M4GrubScrews
Traxxas 5347 Rod Ends with Hollow Balls, Large (set of 12) / https://www.amazon.com/Traxxas-5347-Hollow-Balls-Large/dp/B000BOLVJY/ref=pd_sim_21_2?_encoding=UTF8&pd_rd_i=B000BOLVJY&pd_rd_r=EVVR1SN35F31C2R0E224&pd_rd_w=KGRHX&pd_rd_wg=lZ04X&psc=1&refRID=EVVR1SN35F31C2R0E224 / Good kit: https://www.amazon.com/gp/product/B000BOO7KO/ref=pe_2640190_232748420_pd_te_o_rtpb1_ti/144-6575807-2194132?_encoding=UTF8&pd_rd_i=B000BOO7KO&pd_rd_r=197A5B8YDQCHPBFY03E7&pd_rd_w=Pb4dp&pd_rd_wg=Nninu
1m Brass Tube - 8mm (Note: You need to find a tube that the Traxxas Rod Ends above fit snugly into – see https://www.youtube.com/watch?v=Q7ucXlnLLis&list=UUvFXo_-8dqYWhdq7bQJLh5A ) / Bauhaus
Power Supply..
Screws ...
Medium ..